## Slide 1
Resource Adequacy
Coincident Adjustment Factor Methodology
Miguel Cerrutti
Demand Analysis Office
Energy Assessments Division
R.14-10-010 Workshop
California Public Utility Commission
San Francisco, February 18, 2016

## Slide 2
The problem
Coincidence factor (CF)
Best approaches for calculating CF
Improvements
Outline

## Slide 3
LSE-specific year-ahead and month-ahead load peak forecasts for RA compliance
LSE-specific peak load contribution at the time of CAISO’s peaks
  Accuracy and unbiasedness
Transparency / consistency
The problem

## Slide 4
Ratio LSE’s peaks at time of CAISO coincident peaks (CP) to the LSE’s non-coincident peaks (NCP)
how close LSE’s peak dates/hours are to CAISO’s five top monthly peak dates/hours
        CAISO’s peaks strongly correlated with RES
        LSEs with most RES load - most coincident
  cross-subsidization - RES/COM/IND
CAISO’s peaks - capacity to be procured
  LSEs capacity obligation / costs
Coincidence factor (CF)

## Slide 5
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Time of Peak | 1
GS-2 (Medium Comm. & Industrial) | 0.46706 | 0.46069 | 0.45748 | 0.46064 | 0.48104 | 0.55042 | 0.68797 | 0.80946 | 0.93743 | 0.98741 | 1 | 0.98963 | 0.96987 | 0.95407 | 0.93491 | 0.88937 | 0.84552 | 0.84458 | 0.78274 | 0.73933 | 0.68417 | 0.6251 | 0.56712 | 0.5204
GS-1 (Small Comm.) | 0.51002 | 0.50118 | 0.50059 | 0.50118 | 0.50236 | 0.52476 | 0.57842 | 0.61085 | 0.81309 | 0.95755 | 1 | 0.99175 | 0.95578 | 0.94458 | 0.91804 | 0.89092 | 0.87795 | 0.91097 | 0.79422 | 0.71167 | 0.66274 | 0.59965 | 0.56486 | 0.53892
Residential | 0.575 | 0.525 | 0.52328 | 0.52069 | 0.5319 | 0.5819 | 0.69741 | 0.73621 | 0.66552 | 0.65345 | 0.62328 | 0.59914 | 0.58621 | 0.57931 | 0.57759 | 0.60345 | 0.6819 | 0.88534 | 0.97759 | 1 | 0.99138 | 0.90431 | 0.78017 | 0.66379
Load profile – January
Source: LM 2012

## Slide 6
LSEs’ load profiles display significant variation across time in load shapes and time of peaks
Hourly loads – time-series
    CAISO EMS/OASIS/five top monthly peaks
    CPUC jurisdictional/non-jurisdictional LSEs
  LSE-specific CF
  LSE-composite CF – ESPs/CCAs
    load migration and new ESPs/CCAs
Coincidence factor (CF)

## Slide 7
Historic approach
    CF in the most recent year
    CF over the previous 3 or 5 years / median
    CF weather normalized
    CF trends over time
Forward / forecast approach
    CF in the next year
Best approaches for calculating CF

## Slide 8
CF variation over time
  load composition – RES, COM, IND, H2O
    stable over time - limited migrating load
    heavily drives LSEs peak forecasts
    no easy to correlate to peak – granularity
  weather – temperature
    easy to correlate to peak
    best expected coincidence patterns
Best approach – historic approach

## Slide 9
  Evaluation rule – load profile stability over time and time of peaks
    CF in the most recent year - LSE’s stable load profile / not differ much from CAISO’s times
    CF over three to five previous years – LSE’s unstable load profile / differ much from CAISO’s times
Best approach – historic approach

## Slide 10
      CAISO’s five top monthly weather normalized (WN) coincident peaks
        Time-series multi-step regressive model
        historical weather / Monte Carlo simulation
        Probability of exceedance distribution
      LSEs CF - WN CAISO-coincident peaks
      WN factor - ratio of WN CAISO-coincident peaks and LSE’s median of five top coincident peaks
Best approach – Weather normalized

## Slide 11
      Forward
        new ESPs/CCAs-specific CF
        most recent hourly load shapes–service area
        forecast non-coincident peaks/growth rates
      Forecast – validation
        CF as a function of load factors
        forecast NCP / CP
          NCP / CP weather
          CF / weather differences at NCP/CP times
        forecast CP – WN POE50
          best forecasting practices / reviewing
          methodology adequately / reasonably CP
Best approach – Forward / forecast approach

## Slide 12
Preliminary results
LSE | Moy | CF 0ne-year | CF three-years | CF forward forecast | CF average | WN factor
LSE1 | 5 | .855 | .917 |  |  | 
LSE2 | 2 | .860 | .717 |  |  | 
New CCA | 7 |  |  | .922 | .841 | 
New CCA | 8 |  | .945 |  | .941 | 
 | 7 |  | .752 |  | .846 | 
LSE3 | 8 |  |  |  |  | 1.152
LSE4 | 8 |  |  |  |  | .802
 |  |  | CF RES | CF COM/IND |  | 
LSE5 | 7 | .985 | .985 | .865 | .955 | 

## Slide 13
      Embedding DR impacts in submitted data
      Posting CAISO’s five top monthly coincident peak load dates and hours
      Exploring alternative methods
        be relatively stable over time
        easy to calculate / monitor / apply
      Validation - adjustment
        load migration
        variations in weather and load composition
        forecasting an art as much as a science
Improvements

## Slide 14
And so if …